## Slide 1
VMS Version 3
MS4 & AMI
www.infratec-uk.com

## Slide 2: House Keeping
www.infratec-uk.com
We will be going into the workshop so, please...
Wear appropriate footwear
Stay with group
Signs are on wheels so be careful when working or leaning on signs
You are required to always display your name badge within the building.
No fire alarms planned for today.
Follow myself in the event of an alarm.
Toilets are in reception or across in Unit 8.

## Slide 3: Introduction
Who we are & what we do
www.infratec-uk.com

## Slide 4: Introduction
VMS Limited
V2
Techspan
V2
HILL & SMITH
VMSL V3
www.infratec-uk.com

## Slide 5: Agenda
Equipment overview
Detailed Technical Description
  MS4
  AMI
  Roadside Controller intro
  NRTS Interface (SFP/cat5)
  RSC Navigation
  Software upload
  Download logs
  RMAS Interface
Fault Finding
  Logfile viewer
  logfiles
  Hands on
Q & A practical
www.infratec-uk.com

## Slide 6: Introduction
MS4
AMI
AMI
AMI
CMU
RSC
www.infratec-uk.com

## Slide 7
VMS Version 3
MS4
www.infratec-uk.com

## Slide 8: MS4 Overview
Dimensions | 4440mm x 3160mm x 320mm
Weight | 700kg
Power consumtion | 350W quiesent, 1100W at Level 6
PSUs | 4 x TDK hot swap blades
Character Modules | 96 x RGB V3
Parameter | Value
Display Type | Matrix RGB LEDs
Input Voltage Range | 230-265VAC, 47 - 63Hz
Lantern Type | Virtual on the main display face
Optical Performance | BSEN 12966:2014 C2, L3, R3, B3
Environmental Performance | BSEN 12966:2014 T1, P3, SP2
Reaction to horizontal load | WL8; PL0, DSL0; TDB1
www.infratec-uk.com

## Slide 9: MS4 Access Doors
www.infratec-uk.com

## Slide 10: MS4 PSU Rack
www.infratec-uk.com

## Slide 11: Header
HUB
There is a single Hub Module within the sign face. The Hub interfaces between the Gantry Controller and all the PCBs in the sign. Upon power up (or upon command) the Hub dynamically addresses all Character Modules in the sign. Messages received from the Gantry Controller are echoed out to the other modules as required, with the replies routed back to the Gantry Controller.
Digi IO
A single Digi IO module is installed within the sign. In the MS4 the Digi IO performs the following functions:
Controls the fans within the sign enclosure.
Drives the external status LEDs.
Monitors the PSU rack.
www.infratec-uk.com

## Slide 12: MS4 Power Distribution
www.infratec-uk.com

## Slide 13: MS4 Module Power
www.infratec-uk.com

## Slide 14: MS4 Module Comms
www.infratec-uk.com

## Slide 15: Character Module User LEDS
LED | Purpose | Indication
USER0&1 | Lantern sync | Flashes at 400 msec with the Lantern Sync signal. This signal is synchronised by messages received from the Gantry Controller via the Hub
USER8 | Tx indicator (USARTS 1 to 3) | Transmit Indicator Flashes on replies to messages received from the Gantry Controller, on either the primary or secondary comms channel, via the Hub
USER9 | Rx indicator (USARTS 1 to 3) | Receive Indicator
 |  | Flashes on receipt of messages received from the Gantry Controller, on either the primary or secondary comms channel, via the MS4 Controller / Hub.
USER11 | Heartbeat | Flashes when the software is running.
USER13 | Timer Tick/ Address Configured | Flashes with the 1 msec timer tick signal (appears to be continuously illuminated due to speed)
www.infratec-uk.com

## Slide 16: MS4 ALM
www.infratec-uk.com

## Slide 17: End of Section
Questions
www.infratec-uk.com

## Slide 18
VMS Version 3
AMI
www.infratec-uk.com

## Slide 19: AMI General
Dimensions | 1840mm x 1480mm x 90mm
Weight | 90kg
Power consumtion | 300W Maximum
PSUs | 2x
Character Modules | 4 x MS4 V3, 8 x Red ring segments, 4 x Lanterns
Parameter | Value
Display Type | Matrix RGB LEDs, Red Ring, and Lantern
Input Voltage Range | 80 - 264VAC, 47 - 63Hz
Lantern Type | Physically separate compliant to BS EN 12368:2015 And BSEN 12966:2014
Optical Performance | BSEN 12966:2014 C2, L3, R3
Environmental Performance | BSEN 12966:2014 T1, P3, SP2
Reaction to horizontal load | WL8; PL0, DSL0; TDB1
www.infratec-uk.com

## Slide 20: AMI Mounting and Lifting
www.infratec-uk.com

## Slide 21: Header
Figure 38 - AMI Supplies
www.infratec-uk.com

## Slide 22: Header
www.infratec-uk.com

## Slide 23: AMI Cat5 Cable Routing
FROM THE BACK
www.infratec-uk.com

## Slide 24: Character Module User LEDS
LED | Purpose | Indication
USER0&1 | Lantern sync | Flashes at 400 msec with the Lantern Sync signal. This signal is synchronised by messages received from the Gantry Controller via the Hub
USER8 | Tx indicator (USARTS 1 to 3) | Transmit Indicator Flashes on replies to messages received from the Gantry Controller, on either the primary or secondary comms channel, via the Hub
USER9 | Rx indicator (USARTS 1 to 3) | Receive Indicator
 |  | Flashes on receipt of messages received from the Gantry Controller, on either the primary or secondary comms channel, via the MS4 Controller / Hub.
USER11 | Heartbeat | Flashes when the software is running.
USER13 | Timer Tick/ Address Configured | Flashes with the 1 msec timer tick signal (appears to be continuously illuminated due to speed)
www.infratec-uk.com

## Slide 25: AMI Hub Status LEDs
www.infratec-uk.com

## Slide 26: AMI Hub Status LEDs
LED | Purpose First 5 seconds of operation | Addressing mode Internal addressing of peripherals | Indication After system has addressed and in normal operation | Failure When the HUB is in transparent mode
User LED 0 | Address (MSB) | Off | Flashes at 1HZ | Last state
User LED 1 | Address Success | Flashes at 1HZ whilst addressing | On all the time | State is OFF. Character Module is not addressed Check HUB STATUS LEDS. Check Communications wiring. Power cycle/replace.
User LED 2 | USART RX status | Off | Pulses when a valid internal message is received from channel 2 secondary (Lanterns) ** | State is OFF. Transmission to GC has been affected. Check wiring back to the GC. Check GC for Faults.
User LED 3 | USART Tx Status | Off | Pulses when a message is transmitted on channel 2 secondary (Lanterns) ** | State is OFF. Transmission to Lanterns has been affected. Check wiring back to the Lanterns. Check power and comms cabling to Lanterns.
User LED 4 | USART RX status | Off | Pulses when a valid internal message is received from channel 2 primary (Lanterns) | State is OFF. Transmission to GC has been affected. Check wiring back to the GC. Check GC for Faults.
User LED 5 | USART Tx Status | Off | Pulses when a message is transmitted on | State is OFF. Transmission to Lanterns has been
User LED 6 | USART RX status | Off | Pulses when a valid internal message is received from channel 1 secondary (Tiles or Red Ring) ** | State is OFF. Transmission to GC has been affected. Check wiring back to the GC. Check GC for Faults.
User LED 7 | USART Tx Status | Off | Pulses when a message is transmitted on channel 1 secondary (Tiles or Red Ring) ** | State is OFF. Transmission to RR and Character Module has been affected. Check wiring back to the RR. Check power and comms cabling to RR and Character Modules
User LED 8 | USART RX status | Off | Pulses when a valid internal message is received from channel 1 primary (Tiles or Red Ring) | State is OFF. Transmission to GC has been affected. Check wiring back to the GC. Check GC for Faults.
www.infratec-uk.com

## Slide 27: End of Section
Questions
www.infratec-uk.com

## Slide 28
VMS Version 3
Roadside Controller
www.infratec-uk.com

## Slide 29: Roadside Controller
GANTRY CONTROLLER
www.infratec-uk.com

## Slide 30: Roadside Controller
  NRTS Interface (SFP/cat5)
  RSC Navigation
  Software upload
  Download logs
  RMAS Interface
In this Section
www.infratec-uk.com

## Slide 31: Interfaces
The external data interfaces between the GC and the NRTS infrastructure is achieved in two ways.
The first is through a Small Form-factor Pluggable interface or SFP interface on the rear of the GC. This interface allows either fibre or copper (RJ45 Ethernet) connections to be made.
The second is direct into the bottom RJ45 socket
www.infratec-uk.com

## Slide 32: RSC Navigation
www.infratec-uk.com

## Slide 33: Update Software
Roadside – Follow onscreen instructions
Remote – Via the RMAS interface
www.infratec-uk.com

## Slide 34: AMI – Download Logs
Select this option and enter the Engineers password when asked. Then follow the onscreen instructions to copy the five data items listed below to an USB memory stick
Fault LOGs (current and old – time and date stamped)
Event LOGs (current and old – time and date stamped)
Contents of the address plug (location, addresses, etc.)
Snapshot of Current and Historical faults for each device.
List of software packages and their version numbers which are installed on the Roadside Controller.
These text files will be downloaded and written into a folder ‘rc’ and a subfolder ‘logs’ with a filename including the current time and date.
www.infratec-uk.com

## Slide 35: End of Section
Questions
www.infratec-uk.com